## Slide 1
How the CDR model works
For every ∼1 km² pixel: how much CO₂ does one tonne of crushed basalt durably remove here? A chemical ceiling is reduced by fractional “haircuts,” scaled by application rate, then netted against the project’s own emissions.
1 · Chemical ceiling (stoichiometry)
CDR_max = ( 0.10·(2·44.01/56.08) + 0.07·(2·44.01/40.30) )·1000 ≈ 310 kg CO₂ / t basalt
CaO and MgO each consume 2 mol CO₂; basalt mass fractions 10% / 7%.
2–4 · Fractional haircuts (reactivity, grain, climate, pH, carbonate)
CDR_per_t = CDR_max × 0.20 × (100/d)^0.5 × (f_MAT·f_MAP·f_pH) × (1 − p_ped)
reactive grain climate (capped) exported
f_MAT = clamp(MAT/11°C, 0.3, 3) f_MAP = clamp(MAP/1000mm, 0.3, 3) f_pH = triangular, peak ≈ pH 5
5–7 · Yield, net of emissions, revenue
CDR_gross = rate · CDR_per_t / 1000 (t CO₂ / ha)
CDR_net = max(0, CDR_gross − rate · LCA_per_t / 1000)
revenue = CDR_net · (p_carbon − MRV) NPV regime: × 0.79 (5-yr phasing)
In short: chemistry sets the ceiling (∼310 kg/t); geography — temperature, rainfall, acidity, aridity — decides how much you actually capture (∼80 kg/t at the reference climate).
Notes: 1. Reactive fraction (≈0.20) - biggest cut. Crushed basalt does not fully dissolve within the crediting window; only about a fifth of the stoichiometric maximum actually weathers and releases alkalinity over the project horizon. This single factor removes ~80% of the ceiling and is the most load-bearing - and most scrutinized - assumption in the whole CDR chain. Lewis et al. 2021 (Appl. Geochem. 132:105023), whose temperate mesocosm gives the 0.20 calibration.
2. Grain-size factor - (100/d)^0.5. Reactivity scales with mineral surface area, so finer grinding weathers faster. It is referenced to 100 µm: coarser rock cuts the rate (a true haircut), finer rock raises it. Note the shipped default d = 50 µm actually makes this a multiplier of ~1.41, not a cut - so at the current setting it boosts reactivity. The exponent 0.5 (square-root-of-surface-area) and the grinding-energy cost that trades off against it come from Strefler et al. 2018 (ERL 13:034010), with grain sensitivity also in Lewis et al. 2021.
3. Climate factor - f_MAT × f_MAP × f_pH. Three sub-terms, each able to push reactivity up or down relative to the temperate reference site:
Temperature: clamp(MAT / 11 °C, 0.3, 3) - warm soils weather faster.
Moisture: clamp(MAP / 1000 mm, 0.3, 3) - wet soils weather faster.
Soil pH: a triangular curve peaking near pH 5 - acid-catalyzed dissolution is fastest in moderately acidic soil and falls off in both very acidic and calcareous soils.
A hot, wet, acidic tropical pixel can roughly triple the reference reactivity (before the overall cap at 1); a cold, dry, alkaline one cuts it. Kanzaki et al. 2023 (PNAS Nexus 2:pgad059) and Baek et al. 2023 (Earth's Future 11) for the climate dependence; the pH term rests on silicate-dissolution kinetics in White & Brantley 2003 (Chem. Geol. 202:479) and Brantley et al. 2008. The parameter doc explicitly flags this factor as a v1 empirical proxy.
4. Exported fraction - (1 − p_ped), the aridity haircut. In dry soils a share of the released alkalinity re-precipitates locally as pedogenic carbonate (CaCO₃/MgCO₃), which re-emits the CO₂ instead of exporting it as bicarbonate. Only the exported share is durable CDR. The deduction is binned by aridity (90% lost in hyper-arid soils down to 0% in humid soils). Renforth 2019 (Nat. Commun. 10:1401), Kanzaki et al. 2023, and Reershemius & Suhrhoff 2024 (GCB 30:e17025) for the uncertainty; aridity bands from UNEP 1992, keyed on the CGIAR aridity index of Zomer et al. 2022 (Sci. Data 9:409).

## Slide 2
Key references for methodology & coefficients
Chemistry & stoichiometry
Lewis et al. 2021, Appl. Geochem. 132:105023
Beerling et al. 2020, Nature 583:242 (SI)
Reactive fraction (0.20)
Lewis et al. 2021 — load-bearing calibration
Grain size & grinding (β=0.5, α=1.2)
Strefler et al. 2018, ERL 13:034010
Climate scaling
Kanzaki et al. 2023, PNAS Nexus 2:pgad059
Baek et al. 2023, Earth’s Future 11
pH dependence
White & Brantley 2003, Chem. Geol. 202:479
Brantley et al. 2008, Kinetics of Water-Rock Interaction
Pedogenic-carbonate deduction
Renforth 2019, Nat. Commun. 10:1401
Reershemius & Suhrhoff 2024, GCB 30:e17025
UNEP 1992 (aridity bands); Zomer et al. 2022, Sci. Data 9:409
Net CDR / lifecycle emissions
Eufrasio et al. 2022, Commun. Earth Environ. 3:106
EEA EMEP 2023; UK BEIS 2023; Nemecek & Schnetzer 2011
Time phasing & MRV
Kanzaki et al. 2023; Levy et al. 2024, ES&T 58:17215
Application rate & targeting
Beerling 2020; Baek 2023; Kantola et al. 2023, GCB 29:7012
Aramburu Merlos et al. 2023, Geoderma 432:116421
Full catalogue (S1–S37) with DOIs: docs/erw-parameters.md